## Slide 1: Introduction to the maintenance optimization

## Slide 2: Definitions
Maintenance
  The combination of all technical and administrative actions, including supervision actions, intended to retain an item in, or restore to, a state in which it can perform a required function
Preventive maintenance
  The maintenance carried out at predetermined intervals or according to prescribed criteria and intended to reduce the probability of failure or the degradation of the functioning of an item
Corrective maintenance
  The maintenance carried out after fault recognition and intended to put an item into a state in which it can perform a required function
Maintenance optimization
  Balancing the cost and benefit of maintenance

## Slide 3: Scope of maintenance optimization
Deciding the amount of preventive maintenance (i.e. choosing maintenance intervals)
Deciding whether to do first line maintenance (on the cite), or depot maintenance
Choosing the right number of spare parts in stock
Preparedness with respect to corrective maintenance
Time of renewal
Grouping of maintenance activities

## Slide 4: “Maintenance theory”
The bath tub curve is a basis for choosing maintenance activities
There are two such curves
  The hazard rate for ”local time”
  The failure intensity for ”global time”
Combining the two:

## Slide 5: Performance loss
 The hazard rate for local time
is appropriate for components
such as light bulbs in the signalling
system. Methods are RCM and FMEA
 Rail grinding is a maintenance activity to extend the life length of the rails. JBV method=LCC.
 Point replacement of sleepers is a mean to postpone the complete renewal of sleepers. JBV method=LCC.
 Complete renewal will be required at some point of time. JBV method=LCC.

## Slide 6: Preventive maintenance and RCM
In this course we have main focus on preventive maintenance (PM)
Maintenance optimization is thus more or less the same as establishing an optimal maintenance program
Reliability Centred Maintenance (RCM) is often considered to be the “best” approach in this context
RCM is a systematic consideration of system functions, the way functions can fail, and a priority–based consideration of safety and economics that identifies applicable and effective PM tasks

## Slide 7: Renewal and Life Cycle Cost
As the system deteriorates, traditional preventive maintenance activities could not bring the system to a satisfactory state
Renewal of the entire system, or part of the system is required
The cost of renewal is often very large  we need formalised methods to determine when to perform renewal
In this course we will present methods for optimum renewal strategies based on LCC modelling
The following dimensions are included in the LCC model:
  safety costs
  punctuality costs
  maintenance & operational costs
  cost due to increased residual life length
  project costs

## Slide 8: Effective failure rate
This effective failure rate is the failure rate we would experience if we (preventive) maintain a component at a given level
Notation: E = E()
  E is the effective failure rate = expected number of failure per unit time
   is the maintenance interval

## Slide 9: Effective failure rate and optimization
There are two challenges
  First we want to establish the relation  = E() depending on the (component) failure model we are working with
  Next, we need to specify a cost model to optimise
  The cost model will generally involve system models as fault tree analysis, Markov analysis etc. This enables us to find the optimum maintenance intervals in a two step procedure

## Slide 10: Introductory example
Component model
  Effective failure rate is given by  = E() =  /100
   is the maintenance interval
Total cost of a component failure
  CMCost = 10
  Corrective maintenance cost including loss of production during the repair period
Cost per preventive maintenance action carried
  PMCost = 1
The total cost per unit time
  C() = PMCost /  + CMCost E() = 1 /  +  /10

## Slide 11: Solutions
Graphical
MS Excel Solver
Analytical