## Slide 1: Maintenance Optimization
Understanding Optimization

## Slide 2: Life Data Analysis
Understanding Weibull Analysis

## Slide 3: An Overview of Basic Concepts
In life data analysis (also called "Weibull analysis"), the practitioner attempts to make predictions about the life of all products in the population.
The parameterized distribution for the data set can then be used to estimate important life characteristics of the product such as reliability or probability of failure at a specific time, the mean life and the failure rate.
Life data analysis requires the practitioner to:
  Gather life data for the product.
  Select a lifetime distribution that will fit the data and model the life of the product.
  Estimate the parameters that will fit the distribution to the data.
  Generate plots and results that estimate the life characteristics of the product, such as the reliability or mean life.

## Slide 4: Lifetime Distributions
Statistical distributions have been formulated by statisticians, mathematicians and engineers to mathematically model or represent certain behaviour. The probability density function (pdf) is a mathematical function that describes the distribution.
The equation below gives the pdf for the 3-parameter Weibull distribution.
Some distributions, such as the Weibull and lognormal, tend to better represent life data and are commonly called "lifetime distributions" or "life distributions.“
Other commonly used life distributions include the exponential, lognormal and normal distributions. The analyst chooses the life distribution that is most appropriate to model each particular data set based on past experience and goodness-of-fit tests.

## Slide 5: Parameter Estimation
In order to fit a statistical model to a life data set, the analyst estimates the parameters of the life distribution that will make the function most closely fit the data.
The parameters control the scale, shape and location of the pdf function.
  For example, in the 3-parameter Weibull model
    The scale parameter, η, defines where the bulk of the distribution lies.
    The shape parameter, β, defines the shape of the distribution.
    The location parameter, γ, defines the location of the distribution in time.
Several methods have been devised to estimate the parameters that will fit a lifetime distribution to a particular data set.
Some available parameter estimation methods include
  probability plotting,
  rank regression on x (RRX), rank regression on y (RRY) and
  maximum likelihood estimation (MLE).
The appropriate analysis method will vary depending on the data set and, in some cases, on the life distribution selected.

## Slide 6: Calculated Results and Plots
Once you have calculated the parameters to fit a life distribution to a particular data set, you can obtain a variety of plots and calculated results from the analysis, including:
Reliability Given Time: The probability that a unit will operate successfully at a particular point in time. For example, there is an 88% chance that the product will operate successfully after 3 years of operation.
Probability of Failure Given Time: The probability that a unit will be failed at a particular point in time. Probability of failure is also known as "unreliability" and it is the reciprocal of the reliability. For example, there is a 12% chance that the unit will be failed after 3 years of operation (probability of failure or unreliability) and an 88% chance that it will operate successfully (reliability).
Mean Life: The average time that the units in the population are expected to operate before failure. This metric is often referred to as "mean time to failure" (MTTF) or "mean time before failure" (MTBF).
Failure Rate: The number of failures per unit time that can be expected to occur for the product.
Reliable Life (warranty time). The estimated time when the reliability will be equal to a specified goal. For example, the estimated time of operation is 4 years for a reliability of 90%.

## Slide 7: Calculated Results and Plots
B(X) Life: The estimated time when the probability of failure will reach a specified point (X%). For example, if 10% of the products are expected to fail by 4 years of operation, then the B(10) life is 4 years. (Note that this is equivalent to a reliable life of 4 years for a 90% reliability.)
Probability Plot: A plot of the probability of failure over time. (Note that probability plots are based on the linearization of a specific distribution. Consequently, the form of a probability plot for one distribution will be different than the form for another. For example, an exponential distribution probability plot has different axes than those of a normal distribution probability plot.)
Reliability vs. Time Plot: A plot of the reliability over time.
pdf Plot: A plot of the probability density function (pdf).
Failure Rate vs. Time Plot: A plot of the failure rate over time.
Contour Plot: A graphical representation of the possible solutions to the likelihood ratio equation. This is employed to make comparisons between two different data sets.

## Slide 8: Confidence Bounds
Because life data analysis results are estimates based on the observed lifetimes of a sampling of units, there is uncertainty in the results due to the limited sample sizes.
"Confidence bounds" (also called "confidence intervals") are used to quantify this uncertainty due to sampling error by expressing the confidence that a specific interval contains the quantity of interest.
Two-Sided Confidence Bounds
Lower One-Sided Confidence Bounds
Upper One-Sided Confidence Bounds

## Slide 9: Scope
Weibull analysis includes:
• Plotting the data and interpreting the plot
• Failure forecasting and prediction
• Evaluating corrective action plans
• Test substantiation for new designs with minimum cost
• Maintenance planning and cost effective replacement strategies
• Spare parts forecasting
• Warranty analysis and support cost predictions
• Controlling production processes
• Calibration of complex design systems, i.e., CAD\CAM, finite analysis, etc.
• Recommendations to management in response to service problems
Data problems and deficiencies include:
• Censored or suspended data
• Mixtures of failure modes
• Nonzero time origin
• Unknown ages for successful units
• Extremely small samples (as small as one failure)
• No failure data
• Early data missing
• Inspection data, both interval and probit

## Slide 10: Examples
The following are examples of engineering problems solved with Weibull analysis:
• A project engineer reports three failures of a component in service operations during a three-month period. The Program Manager asks, "How many failures will we have in the next quarter, six months, and year?" What will it cost? What is the best corrective action to reduce the risk and losses?
• To order spare parts and schedule maintenance labor, how many units will be returned to depot for overhaul for each failure mode month-by-month next year? The program manager wants to be 95% confident that he will have enough spare parts and labor available to support the overall program.
• A state Air Resources Board requires a fleet recall when any part in the emissions system exceeds a 4% failure rate during the warranty period. Based on the warranty data, which parts will exceed the 4% rate and on what date?
• After an engineering change, how many units must be tested for how long, without any failures, to verify that the old failure mode is eliminated, or significantly improved with 90% confidence?
• An electric utility is plagued with outages from superheater tube failures. Based on inspection data forecast the life of the boiler based on plugging failed tubes. The boiler is replaced when 10% of the tubes have been plugged due to failure.
• The cost of an unplanned failure for a component, subject to a wear out failure mode, is twenty times the cost of a planned replacement. What is the optimal replacement interval?

## Slide 11: The Weibull Distribution (3 Parameter)
Description
Density function, distribution function and quantile function for the Weibull distribution.
Usage
dweibull3(x, shape, scale, threshold)
pweibull3(q, shape, scale, threshold)
qweibull3(p, shape, scale, threshold, ...)
Arguments
x, q | vector of quantiles
p | vector of probabilities
shape | shape parameter by default 1
scale | scale parameter by default 1
threshold | threshold parameter by default 0

## Slide 12: The Weibull Distribution (3 Parameter)
Details
The Weibull distribution with ‘scale’ parameter alpha, ‘shape’ parameter c and ‘threshold’ parameter zeta has density given by
f(x) = (c/alpha) (((x-zeta)/alpha)^(c-1)) exp(-((x-zeta)/alpha)^c)
The cumulative distribution function is given by
F(x) = 1 - exp(-((x-zeta)/alpha)^c)
Value
dweibull3 gives the density
pweibull3 gives the distribution function
qweibull3 gives the quantile function.
rweibull generates random deviates.