## Slide 1: Business Analytics
Spare part optimization

## Slide 2
Basic concept of inventory management

## Slide 3: Flow diagram for inventory management
Purchase (Purchase procedure )
Store ( Number of stock available)
Consumption (Rate of consumption)
User Division
Nature of materials to be procured
Nature of budget
When to procure
How much Qty to be procured

## Slide 4: Impact of higher & Lower inventory
High Inventory Label
Locking of high working capital that leads to reduction of profit margin
Increases the storing cost
Chance of getting obsolete is high since the technology is improving at faster rate.
Loss of working capital due to damages / obsolesce / pilferages .
No risk of stock out
Low Inventory Label
Risk of loss of production due to non availability of required spare
High lead time can not ascertain the availability of spare at right time
Risk of stock out at any point of time .
Financial loss due to high investment on inventories
Financial loss due to loss of production as result of non availability of stock
Inventory management is a balancing act between financial loss due to high stock and loss of production due to non availability of stock

## Slide 5: Inventory measuring parameters
Inventory Turn over Ratio (ITR) =
(Total consumption for the year )
(Inventory available at the end of the year)
ITR indicates the Inventory condition at any point of time
The ratio is assigned between 1 and 10 depending upon the nature of Materials
Ratio 1 implies number of inventory available is equal to the number of consumption per year.
Ratio 10 implies number of inventory available is only 10% of the consumption per year.
Higher ratio indicates better inventory management

## Slide 6: Classification of materials
Type wise
Cost wise
Budget wise
Rotatable spare – Replaced, Reconditioned & Reused as a whole
Insurance spare – Standby materials for critical equipment
Reconditioning spare – Materials for reconditioning purpose.
Consumables - Materials required for operating & reconditioning
Capital items – Plant and equipments
High value – More than one lakh
Low value – Less than one Lakhs
Capital budget – Plant & equipment : Having asset number, fixed life, Depreciation , Residual value, replaced after expiry of life
Revenue budget – Spares & consumables : No asset number, fixed life & depreciation , having scrap value, used for operating and reconditioning of equipments / system
Application wise
Critical – Without this materials production will be halted
Important - Without this materials production will not be halted but can not be ascertained
Desirable - Without this materials neither production will be halted or affected but it is required for the plant

## Slide 7: 1. Rotatable spare
it is the identical units of the operating machineries
Failed / defective operating units are replaced with this identical unit
Released failed / defective units are repaired / reconditioned at shortest time and kept ready for replacement.
As the spare is always in rotation – it is called rotational spare.
Example : Electrical motor , pump, fan, blower compressor , gear box, transformer , switcher gear etc
Normally this type of spare is maintained within 10% of total population.
Initially it is supplied along with the package as mandatory spare.
On expiry of life, it is disposed at scrap value and a new is procured through revenue budget.
Failed / defective unit
Identical healthy unit
Failed Location
Repaired shop

## Slide 8: 2. Insurance spare
The insurance spare are those vital parts of a machine which have life nearly equal to that of a machine itself and are held as a stand by against any break down .
These stand by units have a high reliability of performance and can be capitalised.
It is supplied by the manufacturer along with the main equipment.
Example : Generator Rotor, Turbine Rotor , Winding of Generator Transformer.
It is some time referred as critical spare for 90% PLF
Part A
Part B
Part C
Part D
Part A
Part B
Part C
Part D
Machine I
Part A
Part B
Part C
Part D
Machine II
Part A
Part B
Part C
Part D
Machine III
Insurance spare parts for all identical machines

## Slide 9: 3. Reconditioning spare
This are the spare parts of the operating machineries
It is used for reconditioning / repair of various machine /equipments
All these items comes under critical category because without these items machine & equipment can not be reconditioned / repaired
These materials are procured under revenue budget
Used materials are disposed at scrap value
Example :Various identical component s of machine & equipments such as motor bearings, impellers of pump & fans, Pulley & hubs of gear box , light fittings (choke, tube, starter), transformer bushings, transformer oil etc.
Number of stock should be sufficient enough to meet out the regular as well as emergency demand.
Stocks are decided based on Consumption rate and Lead time for procurement
Procurement is controlled through EOQ method
Part A
Part B
Part C
Part D
Machine I
Part A
Part B
Part C
Part D
Machine II
Part A
Part B
Part C
Part D
Machine III
Part A
Part B
Part C
Part D
Machine IV
Part A
Part B
Part C
Part D
Reconditioning spare parts for all identical machines

## Slide 10
4. Consumables
This materials are required for reconditioning / repair / operation of various machine /equipments .
Example : Gaskets, Hardwires , Lubricants , fuse , contractor, chemical items, gas etc.
All these items comes under important categories
Consumption rate is very high
Disposal is not assigned with these materials.
Procurement through revenue budget at a fixed interval
Stocks are decided based on Consumption rate and Lead time for procurement
Procurement is controlled through Maxima- Minima basis
Maxima
Minima
Interval for procurement
Interval for procurement
Interval for procurement
Time
Consumption rate
Consumption rate
Consumption rate

## Slide 11: 5. Capital items
The Equipment , Machine, Tools & tackles, Instrument etc which are procured for setting up the plant and are directly or indirectly used for the production of the plant, are known as capital items.
It comes under plant & equipment category and the investment is capitalized.
All these items have asset number , fixed life and depreciation
During service life depreciation amount is collected and kept aside for the procurement of new item at the end of life.
At the end of life, it is disposed (survey reported) at residual ( salvage ) value.
New item is procured from the depreciation fund against the disposal of the old items.
Since procuring of new item is done from the depreciation fund it is considered as the reinvestment of the capital fund and therefore it can not be capitalized
Procurement is through depreciation fund under capital budget and is done at the end of service life .
Residual value
Salvage value (10%)
Depreciation fund (NV – SV)
Asset life in years
15
0
Fund is used for procurement
New Items
Installation after disposing old items

## Slide 12: Inventory controlling methods
×
=
×
=
High Value
Low consumption rate
Economic order Quantity
Low Value
High consumption rate
Maxima Minima
Materials (Reconditioning spares & consumable items)

## Slide 13: Economic order quantity (EOQ)
Economic Order Quantity ( EOQ) =
(Average yearly Consumption X Lead Time [in years] ) + Emergency Stock – Stock on hand
Transformer oil
1. Average yearly consumption = 80KL
2. Lead time for procurement = 1 year
3. Emergency stock = 80 KL
4. Stock in hand = 100 KL
5. EOQ = (80 x 1) + 80 -100 = 60 KL
16 mm2 copper cable
1. Average yearly consumption = 1000 Mtr
2. Lead time for procurement = 1 year
3. Emergency stock = 100 Mtr
4. Stock in hand = 20 Mtr
5. EOQ = (1000 x 1) + 100 -20 = 1080 Mtr
Conveyor roller
1. Average yearly consumption = 300 Nos
2. Lead time for procurement = 1 year
3. Emergency stock = 50 Nos
4. Stock in hand = 10 Nos
5. EOQ = (300 x 1) + 50 -10 = 340 Nos
Roller Bearing ( NU320)
1. Average yearly consumption = 20 Nos
2. Lead time for procurement = 1 year
3. Emergency stock = 6 Nos
4. Stock in hand = 10 Nos
5. EOQ = (20 x 1) + 6 -10 = 16 Nos

## Slide 14: Maxima - Minima
2. Re order Level (ROL)
[ At this level next order to be placed]
= (Max consumption X Maximum lead time)
3. Minimum order Level (MIOL)
[This is the quantity to be maintained at the store to prevent stock out condition]
= ROL - (Average consumption X Average lead time)
4. Maximum order Level (MAOL)
[This is the quantity above which stock is not allowed to exceed]
= ROL + EOQ - (Minimum consumption X Minimum lead time)
1. Economic order quantity ( EOQ)
[ This is the quantity to be procured]
= (Minimum consumption X Maximum lead time)
5. Avg inventory (MAOL)
[This is the quantity always available in the store ]
= (MIOL + MAOL)/2

## Slide 15: Maxima - Minima
 | Max | Mini | Avg
Yearly consumption pattern ( C ) | 75 Nos | 25 Nos | 50 Nos
Lead time for procurement (LT) | 0.5 Yr | 0.3 Yr | 0.4 Yr
 | Formula | Qty
EOQ | Mini( C ) x Max ( LT ) | (25 x 0.5) = 13 Nos
ROL | Max ( C ) x Max ( LT) | (75 x 0.5) = 38 Nos
MIOL | ROL – [ Avg ( C ) x Avg ( LT) ] | (38 – 20) = 18 Nos
MAOL | ROL + EOQ – [Mini ( C ) X Mini ( LT)] | (38+13 – 8) = 43 Nos
Avg Inventory | (MIOL +MAOL)/2 | (18 +43)/2 = 31 Nos
MIOL
MAOL
18
43
ROL
38
EOQ = 13

## Slide 16
Effective Spare Parts Management: 8 Rules

## Slide 17: Eight rules for efficient SPM
Go for preventive maintenance!
Eliminate process problems
Segment your spare parts portfolio
Evaluate spare parts criticality
Spare parts management starts with good forecasting
Use special methods for intermittent demand items
Consider the whole life cycle of your equipment
Implement a good information system for spare parts and maintenance inventory management
8

## Slide 18: Go for preventive maintenance

## Slide 19: Go for preventive maintenance!
STANDARD PLANNED
PLANNED
MAINTENANCE
CORRECTIVE
(REPAIRS)
UNPLANNED
PREDICTIVE
PROACTIVE
DEFFERED CORRECTIVE
PLANNED PROCUREMENT
INVENTORY MANAGEMENT

## Slide 20
Prevention or correction?
Number of preventive X corrective actions
Downtimes due to corrective maintenance – repairs
Total maintenance cost

## Slide 21: Eliminate process problems

## Slide 22
LIFE CYCLE OF A SP IN A COMPANY

## Slide 23
Eliminate process problems
SP NEED IDENTIFICATION
There is no direct responsibility of maintenance engineers/technicians for “their” items and spare parts levels.
REQUEST FOR ORDER
RFO created by someone else, not by the technician who had identified the need.
The step of creating RFO may not be necessary in the process.
RFO APPROVAL
How often are RFOs approved? Who approves?
Is RFO approved by means of IS workflow or by signing a paper copy? Alternatively, are both ways needed?
After RFO is approved, the issued order must be approved again.
Too many approvers, complicated approval procedure and hierarchy of responsibilities.
Approving on high levels of management.

## Slide 24
Eliminate process problems
PROCUREMENT
Insufficient information available to procurement, poor spare parts identification – the buyer hardly knows what should be bought, additional communication with maintenance technician is needed.
Missing or incomplete procurement specification in the IS.
RECEPTION
Problems with missing (undelivered) documentation for the received material (certificates, declarations).
Only “paper-based” archiving of spare parts documentation.
Problems to find documentation when needed.
WAREHOUSING
Insufficient identification of spare parts in the warehouse.
Problems with finding items stored in the warehouse.
Inventory count discrepancies, physical stock different from information system data.
Non-real value of stock in the information system.
Existence of out-of-system stocks.

## Slide 31
Eliminate process problems
CONSUMPTION
Slow spare part issues in case of sudden need.
Issued spare parts are not consumed in fact. What happens then?
Consumption of external material even in case the part is on stock.
WAREHOUSE RETURNS AND REFURBISHED SPARE PARTS
Refurbished parts return to warehouse while new are bought.
Accounting price of refurbished items is much higher (or lower) than the non-realistic value of items on stock.
Problematic or impossible returns of parts issued but not consumed.
Insufficient control of parts dismantled from the maintained object (the information system has no information about these).

## Slide 32: Segment your spare parts portfolio

## Slide 33
WHEN?
HOW MANY?
WHEN?
HOW MANY?
Strategic segmentation of spare parts
CONSIGNATION
CONSIGNATION
CONSIDER CONSIGNATION
CONSIDER CONSIGNATION
BUY
BUY
BUY
BUY
CONSIDER CONSIGNATION
CONSIGNATION
BUY BACK
BUY
TYPE OF FORECAST
CONSUMPTION FREQUENCY
VALUE

## Slide 34: Evaluate spare parts criticality

## Slide 35: Criticality assessment phases
Preliminaryassessment
Technician
Hold on stock
Potentially critical part
Do not stock
Advanced methods to set optimal levels
Criticality assessment
Technician
Consume
Sell or
Scrap
Optimum
SP level

## Slide 36
  Effects of failure
  Technical places
  Consequences of unavailability
  Delivery time
  Repairability
  Possibility of maintenance planning
  Part lifespan
  Failure probability
  Failure characteristics
  Failure anticipation
  Price
  % cost of capital
Cost of inventory holding
Failure probability
Impacts of spare part unavailability
Leadtime and other parameters
Evaluate spare parts criticality

## Slide 37: Spare parts management starts with good forecasting

## Slide 38: Quantitative methods x Common sense
Quantitative methods
Common sense

## Slide 39: Quantitative methods x Common sense
Quantitative methods
Common sense
Unexplained / Random
Uncertainty of future consumption
Maximize
Make efficient
Minimize

## Slide 40: Forecasting step-by-step
Visualisation of time series
For better understanding of the time series
Calculation of accuracy
Absolute and relative errors, evaluation on testing season
Calculation of forecasts using all available methods
Selection of the best method
Best accuracy and reliability
1
3
2
4
Notes: 39

## Slide 41: Which method is the best for spare parts?
Chart: 
| Konstantní model | Regresní model | Holtovo exp. vyrovnání | Jednoduché exp. vyrovnání | Klouzavý průměr | Winters | Forecasting není možný
 | 0.0068562 | 0.0070579 | 0.024198 | 0.032265 | 0.048397 | 0.088728 | 0.78645
???
Notes: 40

## Slide 42: Use special methods for intermittent demand items

## Slide 43: Spare parts – intermittent demand
Weekly consumption history (weeks)
Weekly spare part consumption (pieces)
QUESTION: What reorder level should be set in order to ensure required availability of a spare part?

## Slide 44: Bootstrapping
Bootstrapping = random sampling from history of consumptions.
SP consumption for lead-time period is sampled from history
Sample 1: Consumption in 6 weeks = 5 pcs
Weekly SP consumption
Weekly consumption history (weeks)
Example: SP lead time is 6 weeks

## Slide 45: Bootstrapping
Vzorek 2: Spotřeba za 6 týdnů = 0 ks
Sample 2: Consumption in 6 weeks = 0 pcs
Weekly consumption history (weeks)
Spare part consumption (pieces)

## Slide 46: Bootstrapping
Vzorek 3: Spotřeba za 6 týdnů = 12 ks
Sample 3: Consumption in 6 weeks = 12 pcs
Weekly consumption history (weeks)
Weekly SP consumption

## Slide 47: Bootstrapping
Vzorek 4: Spotřeba za 6 týdnů = 2 ks
Sample 4: Consumption in 6 weeks = 2 pcs
Weekly consumption history (weeks)
Weekly SP consumpiton

## Slide 48: Example of 100 000 simulations of SP consumption
Target: SP availability (Service level) = 99%
OPTIMUM INVENTORY= 9 PCS
Consumption during leadtime (pcs)
Cummulative probability of consumption
Frequencies of consumption
(from simulation)

## Slide 49: Bootstrapping application – a case study
99.9% availability
Original inventory: 17 000 EUR (49 pcs)
Spare part lead-time: 32 days
Recommended inventory
29 pcs
10 000 EUR
Savings
7 000 EUR
Intermittent demand

## Slide 51
Life cycle thinking: Consider the whole life cycle of your assets

## Slide 52: Life cycle thinking: Consider the whole life cycle of your assets

## Slide 53
Bermuda triangle of asset management
Life cycle thinking: Consider the whole life cycle of your assets

## Slide 54
PROCUREMENT
INSTALLATION
OPERATION
MAINTENANCE
RENOVATION
DISPOSAL
COST
COST
COST
COST
COST
PROFIT?
PROFIT
MAINTENANCE CREATES VALUE!
ASSET LIFE CYCLE

## Slide 55
Asset life cycle (Kari Komonen, EFNMS EAMC)
INVESTMENT
UTILIZATION
$
$

## Slide 56
PROCUREMENT
INSTALLATION
OPERATION
MAINTENANCE
RENOVATION
DISPOSAL
COST
COST
COST
COST
COST
PROFIT?
PROFIT
MAINTENANCE CREATES VALUE!
ASSET LIFE CYCLE

## Slide 57: Efficient spare parts management Conclusions

## Slide 58: Efficient spare parts management – 8 rules
Preventive maintenance
Processes without problems
Segment your SP portfolio
Assess the criticality
Good forecasting
Special methods for intermittent demand items
Asset life cycle
Good information system
Notes: 57

## Slide 59: Good information system for spare parts management
Quantitative methods
Common sense
Unexplained / Random
Maximize!
Make efficient!
Minimize!
Forecasting
Inventory levels
Ordering
Input of technicians and procurement
Criticality analysis
Forecast accuracy and reliability

## Slide 60
Spare parts management involves balancing the timely availability of spares and minimizing capital blocked in overall inventory. Poor spare parts management directly leads to poor asset availability and plant reliability. Organizations, faced with the complexity of spare parts optimization, must have better control over MRO inventory.
Comprehensive data analysis develops greater understanding and visibility of all aspects of spare parts management. The insight obtained by in-depth data analysis can help organizations build and execute better strategies.

## Slide 61: Challenges in spare parts management:
Ensuring timely spares availability to ensure greater asset availability
Getting timely alerts on stock-outs of critical spares
Identifying exceptions, outliers and issues for better inventory control
Monitoring inventory turns, spillage and carrying costs
Understanding blocked capital and inventory carrying cost
Making informed financial planning and budgeting decisions
Optimizing overall MRO inventory

## Slide 62: How data analysis helps in spare parts optimization?
Identification and management of slow moving, non moving and obsolete items
Understand physical placement options for items to increase store room efficiency
Monitoring of spare part availability for upcoming PM’s
Understand consumption patterns and capital investment by performing ABC Analysis
Critically rank and categorize items based on various procurement constraints and options
Manage inspections, cycle counts and expiry
Set min, max levels
Determine economic order quantity (EOQ)
Define stocking policies for capital and rotating assets or subassemblies
Provide supporting analysis for building comprehensive strategies, executing strategic action plans and monitoring outcomes for timely adjustments
Optimize inventory by balancing financial and reliability variables

## Slide 63: Business Benefits
Increase productivity
Reduce compliance risks
Lower maintenance cost
Gain visibility across the enterprise with well defined performance metrics
Reduce unplanned downtime, increase reliability of critical equipments
Spare parts optimization
Determine root causes of non-conformities
Increased ROA

## Slide 64: IT Benefits
Reusable DW data models, ETL, metrics, scorecards, reports, KPI’s and OLAP
Bridge gap between end user's perceived needs and actual business requirements
Awareness of data analysis capabilities
Improved data quality
Ability to integrate other data sources outside of EAM for more comprehensive reporting
Better leveraging of transaction data and IT infrastructure
Time to focus on other projects

## Slide 65: Our methodology and analysis techniques
Determine Stock out Risk/Probability for critical assets spares using Weibull analysis
Identify bottlenecks in the spares supply chain process by applying six-sigma analysis.
Understand procurement efficiency by tracking KPIs for each PR
Optimize stock holding with FSN and ABC Analysis.
Forecast erratic spares demand by using Croston/ARIMA method.
Identify slow moving and non moving items.
Determine spare parts cost for budgeting purposes based on the Croston's Method.
Find optimum spare parts inventory level.
Understand demand patterns by classification based on Smooth. Irregular, Slow-moving. Mildly Erratic, Highly Erratic etc

## Slide 66
Case study description (as heat exchanger)
Problem statement
Stepwise description
R script
graphs
Concluding statements

## Slide 67: Design Thinking
Ask the participants what kind of problems related to their industry can be solved using this concept.

## Slide 68: Question & Answers

## Slide 69: THANK YOU
Copyright © 2016 Defour Analytics Pvt. Ltd